        Report
        Syniavskyi V.V. 20-04-15.
    Now we will test VAD programs, which I made earlier: sqwenrgyVAD, weakfricdetVAD, avtopeak2VAD,
stat1VAD. We will use two digital audio files: 'prob1.wav' (Fig.1.) and 'Speech.wav' (Fig.2.).

    File 'prob1.wav'contains sample (vector column ), which has dimension 80896. Each value of this sample is an amplitude of sound signal in db. The frequency of audio recording is 44100 H. Every period of this wave corresponds to one point of the sample. The continuance of this recording is about 2 seconds (80896/44100). (Really, I said word "seven".)
    Each VAD program divides whole sample on frames - 10 ms everyone. Each frame in 'prob1.wav' file will
contains 441 points of sample.
     File 'Speech.wav' contains sample, which has dimension 152608, frequency 16000H, and continuance
about 9.5 seconds. (Voice said "A quick brown fox jumps over lazy ducks".) Each frame in this file will contains 160 points of sample.
     Each VAD progpam determins for every frame; " Is there voice ,or is not". The result is function vad(x):
 vad(x)=1, if point x belongs frame with voice, otherwise vad(x)=0. You can see the graphics for vad(x)
 functions of all our programs on Fig.3. and Fig.4.(sqwenrgyVAD - black line, weakfricdetVAD - magenta line, avtopeak2VAD - cyan line, stat1VAD - red line.) For more visibility I multiplied every vad function (exept sqwenrgyVAD) on different coefficients.
     As can we see at Fig3.(and Fig11) magenta(weakfricdetVAD) line covers blue line exactly. Stat1VAD lost one frame, sqwenrgyVAD lost two frames. avtopeak2VAD lost 10 frames and added 2 false . Our program (VAD_comparing_15_04_15_.m) can count number frames with voice, and it shows:

   name numberVoiceFrames
    ________________ _________________

    'sqwenrgyVAD' 38
    'weakfricdetVAD' 40
    'avcorpeakVAD' 32
    'stat1VAD' 39
    On aurally, here, all (four) VADs give same results, I can not hear differance. Sound is good.
    Now let nandle second record, using our VADs.
    As can we see at Fig4.(and Fig10), again, magenta (weakfricdetVAD) line covers blue line exactly. Stat1VAD lost 3 frame, and added 7 false frames, sqwenrgyVAD lost two frames. avtopeak2VAD lost 39 frames, and added 2 false frames.
        name numberVoiceFrames
    ________________ _________________

    'sqwenrgyVAD' 286
    'weakfricdetVAD' 293
    'avcorpeakVAD' 256
    'stat1VAD' 297
    On aurally, here, all (four) VADs give same results,too. I can not hear differance. Sound is good.
   Now we will add white noice (red on Fig5a and Fig5b), more and more with every time(Fig8a - Fig9b).
   At first, we will add N = randn(X2)* 0.01. Where randn(X2) is vector with same dimension as vector X2 ,
and its values are random values, with classical normal distribution.
   As we see at Fig5b N has amplitude about 0.035db, for compare real noice in X1 has amplitude about 0.02db,
noise in X2 has amplitude about 0.005db.X2 is very clear signal. I took it from special library (see my earlier notes).
    I wrote special program (VAD_comparing_15_04_15_.m) to test our VADs in conditions with different noise ratio in signal.
   At first we use signal X2( 'Speech.WAV) .And we run the script-function (VAD_comparing_15_04_15_.m)
 by call: A1 = VAD_comparing_15_04_15_('Speech.WAV', 0, 0.01, 0.02, 0.03); T = struct2table(A1).
  And we get graphic of four vad(t) functions for X2 + N signal(Fig10a), and also we get a statistical
table:

       name numberVoiceFrames numberLostFframes ratio_Errors_to_Voice_Fframes
    ________________ _________________ __________________________ _________________ _____________________________

    'sqwenrgyVAD' 286 164 0.57343
    'weakfricdetVAD' 293 141 0.48123
    'avcorpeakVAD' 256 132 0.51563
    'stat1VAD' 297 124 0.41751
       On aurally, here,
  'weakfricdetVAD' has one defect: we can not hear sound 's' at the end of word 'ducks'.
  'avcorpeakVAD' has next defects: we hear interference at the end of word 'quick'.
        'sqwenrgyVAD' has next defects: we can not hear sounds 'k' and 's' at the ends of words 'fox' and
        'ducks'.
        'stat1VAD' has good sound.

     Then we run the script-function (VAD_comparing_15_04_15_.m) by call: A1 =
VAD_comparing_15_04_15_('Speech.WAV',0,0.02,); T = struct2table(A1).
  And we get graphic of four vad(t) functions for X2 + 2*N signal(Fig10b), and also we get a statistical table:
       name numberVoiceFrames numberLostFframes ratio_Errors_to_Voice_Fframes
    ________________ _________________ __________________________ _________________ _____________________________

    'sqwenrgyVAD' 286 210 0.73427
    'weakfricdetVAD' 293 163 0.55631
    'avcorpeakVAD' 256 214 0.83594
    'stat1VAD' 297 169 0.56902
   On aurally, here ,
   'weakfricdetVAD' has two defects: we can not hear sounds 'k' and 's' at the end of word 'ducks'.
   'avcorpeakVAD'	gives bad sound: a lot of interference at the end of every word.
   'sqwenrgyVAD'	has next defects: we can not hear sounds 'k' and 's' at the ends of words 'fox' and 'ducks'
        and ends of others words are cut.
    'stat1VAD' has one defect: we can not hear sound 's' at the end of word 'ducks'.
    Then we run the script-function (VAD_comparing_15_04_15_.m) by call: A1 =
VAD_comparing_15_04_15_('Speech.WAV',0,0.03,); T = struct2table(A1).
  And we get graphic of four vad(t) functions for X2 + 3*N signal(Fig10c), and also we get a statistical table:
      name numberVoiceFrames numberLostFframes ratio_Errors_to_Voice_Fframes
    ________________ _________________ __________________________ _________________ _____________________________

    'sqwenrgyVAD' 286 255 0.89161
    'weakfricdetVAD' 293 175 0.59727
    'avcorpeakVAD' 256 243 0.94922
    'stat1VAD' 297 175 0.58923
     On aurally, here ,
'weakfricdetVAD' has next defects: we can not hear sounds 'k' and 's' at the ends of words 'fox' and
        'ducks'.
        'sqwenrgyVAD' gives bad sound: the ends of all words are cut.
        'stat1VAD' has next defects: we can not hear sounds 'k' and 's' at the ends of words 'fox' and 'ducks'.
    As we see, at last, 'stat1VAD' and 'weakfricdetVAD' have better result than	'sqwenrgyVAD' and
'avcorpeakVAD' and is the best.
   Then, we use signal X1( 'prob1.WAV) And we are run the script-function (VAD_comparing_15_04_15_.m)
 by call: A1 = VAD_comparing_15_04_15_('prob1.WAV',0,0.01,0.02,0.03); T = struct2table(A1).
 And we get graphic of four vad(t) functions for X1 + N signal(Fig11a), and also we get a statistical table:
        name numberVoiceFrames numberLostFframes ratio_Errors_to_Voice_Fframes
    ________________ _________________ __________________________ _________________ _____________________________

    'sqwenrgyVAD' 38 7 0.18421
    'weakfricdetVAD' 40 1 0.025
    'avcorpeakVAD' 32 23 0.71875
    'stat1VAD' 39 0 0.025641

Then we run the script-function (VAD_comparing_15_04_15_.m) by call: A1 =
VAD_comparing_15_04_15_('Speech.WAV',0,0.02,); T = struct2table(A1).
 And we get graphic of four vad(t) functions for X1 + 2*N signal(Fig11b), and also we get a statistical table:
        name numberVoiceFrames numberLostFframes ratio_Errors_to_Voice_Fframes
    ________________ _________________ __________________________ _________________ __
    'sqwenrgyVAD' 38 19 0.5
    'weakfricdetVAD' 40 2 0.05
    'avcorpeakVAD' 32 27 0.84375
    'stat1VAD' 39 0 0.025641
On aurally, here ,
        'avcorpeakVAD' has very bad sound (only 's' and interference).
'sqwenrgyVAD' has next defects: there are interference.
        'stat1VAD' and 'weakfricdetVAD' have good sound.
       Then we run the script-function (VAD_comparing_15_04_15_.m) by call: A1 =
VAD_comparing_15_04_15_('Speech.WAV',0,0.03,); T = struct2table(A1).
  And we get graphic of four vad(t) functions for X1 + 3*N signal(Fig11c), and also we get a statistical table:
        name numberVoiceFrames numberLostFframes ratio_Errors_to_Voice_Fframes
    ________________ _________________ __________________________ _________________
    'sqwenrgyVAD' 38 26 0.68421
    'weakfricdetVAD' 40 8 0.2
    'avcorpeakVAD' 32 30 0.9375
    'stat1VAD' 39 0 0.025641
    On aurally, here ,
        'avcorpeakVAD' has very bad sound (only 's' and interference).
'sqwenrgyVAD' has next defects: We can hear only part 'se...' of word 'seven'.
        'stat1VAD' and 'weakfricdetVAD' have good sound.
    As we can see (Fig9.a) , in this case, ratio voice/noise is (0.78-0.14)/0.14 = 4.57.
     In whole, we can make conclusion: The VADs 'stat1VAD' and 'weakfricdetVAD' are more appropriate for our work. The 'stat1VAD' is the best.